## Slide 1: E&M Auto Routing Design with AI - ARAI
G&K Consultancy Ltd. AND SZU

## Slide 2: Algorithm output: case example
Revit input data
East Section
West Section
Plan
Φ250mm GraFlow
1000mmx400mm MVAC
Problem:
  different types of pipes occupy same space
  Some law might be violated (e.g. 30m’ law)
  Might not be enough space (height)
2000mmx400mm MVAC
Φ250mm GraFlow

## Slide 3
CAD input data

## Slide 4: Algorithm output: case example
Input explanation:
  We transfer the pipes into formatted data to input to the algorithm
    This step can be carried out by software once it is developed
  All pipes in the formatted data will not have height information in input
  The algorithm will do (most important parts):
  Locate all pipes, including height information, where to turn to avoid collision / to be ‘行气’
  Shape changing if allowed and necessary
  Through the beam if allowed and necessary
  Warning if necessary

## Slide 5: Algorithm output: case example
  In the Revit input figure, all pipes are random draw (height and place in the corridor) above suspended ceiling, therefore there will be a lot of collision, or might look stupid

## Slide 6: Algorithm output: case example
Output explanation
  The pipe routing result can be read by an engineer to get Revit
    This step can be carried out by software once it is developed

## Slide 7: Algorithm output: case example
Program output
East Section
West Section
Plan
Φ250mm GraFlow
1000mmx400mm MVAC
2000mmx400mm MVAC
We will go back to explain this case latter, now we move on to see how it works

## Slide 8: Algorithm output: functional examples
Some functional examples:
  Spacing between pipes (A,B,C)
  Crossing over and size changing (A,B,C)
  30m’s law for gravity drainage pipes
  Through beams (A,B)
  Automatic aligning

## Slide 9: Functional examples: Spacing A
Revit input data
East Section
West Section
Problem: no space between pipes
Φ250mm GraFlow
Plan

## Slide 10: Functional examples: Spacing A
CAD input data
Problem: no space between pipes, especially when drawing under CAD format

## Slide 11: Functional examples: Spacing A
Formatted input
3 pipes in the same space in the input, to be routed to the corrected place by the algorithm
Begin and End: height information is ‘none’ because that is what we need to find out; 3 pipes in the same space and that is what to be tackled
All the types of pipes, including the shape, type, insulation, installation spaces, etc.
For more details: see ‘HH FSE rule based engg 20191127 (amended by RW2)-0.xls’, Z8—Z14, M2—M11, PD10—PD12, etc.

## Slide 12
Formatted input
Here is some part of the modeling and program, to show how to add the installation space:
For different types of pipes, different space is allocated
All the types of the pipe, included the shape, type, insulation, installation spaces, etc.

## Slide 13: Functional examples: Spacing A
Routing procedure
This short video shows the procedure of routing

## Slide 14: Functional examples: Spacing A
Input: pipes not routed
Program output: pipes in correct space
Different pipes occupy different space
Begin height: as high as possible
End height: with appropriate slope

## Slide 15: Functional examples: Spacing A
Program output
Visualization step (without Revit): we draw all the pipes in an array, for the figuring

## Slide 16: Functional examples: Spacing A
Program output
Color in yellow refers to the space
Color in red refers to the pipes with insulation layer
Note: we draw a cube instead of the circle because it is hard to draw a circle in such point map, however, the pipes is marked to be a circular tube therefore it can be correctly read by Revit.

## Slide 17: Functional examples: Spacing A
Program output
Plan
East Section
West Section
Φ250mm GraFlow

## Slide 18: Functional examples: Spacing B
Revit input data
East Section
West Section
Plan
Problem: no space between pipes; when installation space added, one layer is not enough for all pipes
Φ600mm GraFlow

## Slide 19: Functional examples: Spacing B
Formatted input

## Slide 20: Functional examples: Spacing B
Program output
Visualization step (without Revit): we draw all the pipes in an array, for the figuring
这里放数字那个图

## Slide 21: Functional examples: Spacing B
Program output
Can divide them to two layers with correct spacing
Flag1：单层空间不足
第一层的剩余空间不够排布GraFlow_3，排在第二层

## Slide 22: Functional examples: Spacing B
Program output
East Section
West Section
Plan
Φ600mm GraFlow

## Slide 23: Functional examples: Spacing C
Revit input data
East Section
North Section
Plan
Problem: no space between pipes; when installation space added, not enough space for all pipes;
Φ600mm GraFlow

## Slide 24: Functional examples: Spacing C
Formatted input

## Slide 25: Functional examples: Spacing C
Program output
The difference between 144 and 98 indicates that there is not enough space above the suspended ceiling
这里放数字那个图

## Slide 26: Functional examples: Spacing C
Program output
We use one block in this figure to represent 10mm, therefore in this case, the ceiling requires 460mm more
Flag6：管线排布高度不够，穿过假天花
GraFlow_3穿过假天花，需要增加（144-98）*10mm=460mm高度
Flag1：单层空间不足
第一层的剩余空间不够排布GraFlow_3，排在第二层

## Slide 27: Functional examples: Spacing C
Program output
East Section
North Section
Plan
Φ600mm GraFlow

## Slide 28: Functional examples: Crossing over A
Revit input data
East Section
North Section
Plan
Problem: blue/yellow pipes go through same space (Gravity Flow)
Φ400mm GraFlow
Φ300mm GraFlow

## Slide 29: Functional examples: Crossing over A
Formatted input

## Slide 30: Functional examples: Crossing over A
Program output
Visualization step (without Revit): we draw all the pipes in an array, for the figuring
这里放数字那个图

## Slide 31: Functional examples: Crossing over A
Program output
In current stage: when Gravity Flow pipe goes down, unless necessary, it will not goes up again
Flag0：两管十字交叉相撞
两管十字交叉，GraFlow_2下折避开GraFlow_1

## Slide 32: Functional examples: Crossing over A
Program output
East Section
North Section
Plan
Φ400mm GraFlow
Φ300mm GraFlow

## Slide 33: Functional examples: Crossing over A
Revit input data
East Section
West Section
Plan
Problem: blue/yellow pipes go through same space (MVAC)
1500mmx700mm MVAC
600mmx600mm MVAC

## Slide 34: Functional examples: Crossing over A
Formatted input

## Slide 35: Functional examples: Crossing over B
Program output
Visualization step (without Revit): we draw all the pipes in an array, for the figuring
这里放数字那个图

## Slide 36: Functional examples: Crossing over B
Program output
For MVAC: goes down, and then up again
If there is not enough space, it will change the shape of the pipe
When go up, unless necessary, the shape will not be changed back
Flag0：两管十字交叉相撞
Falg7： MVAC_2空间高度不足
两管十字交叉，MVAC_2下折避开MVAC_1再上折
风管改形状，横截面积不变

## Slide 37: Functional examples: Crossing over B
Program output
East Section
North Section
Plan
1500mmx700mm MVAC
600mmx600mm MVAC

## Slide 38: Functional examples: Crossing over C
Revit input data
East Section
North Section
Plan
Problem: blue/yellow pipes go through same space (mixed Gravity Flow & MVAC)
600mmx600mm MVAC
Φ700mm GraFlow

## Slide 39: Functional examples: Crossing over C
Formatted input

## Slide 40: Functional examples: Crossing over C
Program output
Visualization step (without Revit): we draw all the pipes in an array, for the figuring
这里放数字那个图

## Slide 41: Functional examples: Crossing over C
Program output
Flag7：MVAC_1空间高度不足
风管改变形状，横截面积不变
两管十字交叉，MVAC_2下折避开GraFlow_1再上折
Flag9：水管与风管十字交叉相撞

## Slide 42: Functional examples: Crossing over C
Program output
这里放Revit结果图
600mmx600mm MVAC
Φ700mm GraFlow
East Section
North Section
Plan

## Slide 43: Functional examples: 30m’s law
Revit input data
East Section
West Section
Plan
Problem: Gravity Flow longer than 30m
Φ250mm GraFlow
Problem: Gravity Flow longer than 30m

## Slide 44: Functional examples: 30m’s law
Formatted input

## Slide 45: Functional examples: 30m’s law
Program output
Visualization step (without Revit): we draw all the pipes in an array, for the figuring

## Slide 46: Functional examples: 30m’s law
Program output
Program output
Flag8：水管长度超过30m
GraFlow_1在从起点开始，长度30m处下降200mm
We use one block in this figure to represent 10mm, therefore in this case, the drop is (69-49) *10mm = 200mm

## Slide 47: Functional examples: 30m’s law
Program output
East Section
West Section
Plan
Φ250mm GraFlow

## Slide 48: Functional examples: Go through the Beam A
Revit input data
East Section
West Section
Plan
Φ60mm GraFlow
Problem: a lot of small pipes, they are required to be as high as possible (close to the ceiling), therefore should go through the beam

## Slide 49: Functional examples: Go through the Beam A
Formatted input

## Slide 50: Functional examples: Go through the Beam A
Program output
Visualization step (without Revit): we draw all the pipes in an array, for the figuring
这里放数字那个图

## Slide 51: Functional examples: Go through the Beam A
Program output
In current stage: the pipes will go through the beam, if they can, within 1/3 – 2/3 space.
1/3
2/3
Not larger than 250mm
Flag3：水管直径小于250mm穿梁
10条水管直径都小于250mm，并且全部排列后总高度不超过250mm，全部进行穿梁处理
横梁中剩余空间不足，GraFlow_9和GraFlow_10排在横梁的第二层
Flag1：单层空间不足

## Slide 52: Functional examples: Go through the Beam A
Program output
East Section
West Section
Plan
Φ60mm GraFlow

## Slide 53: Functional examples: Go through the Beam B
Revit input data
East Section
West Section
Plan
10000
10000
3070
3500
3430
Problem: pipes with Dia. <= 250mm can go through the beam, and those with Dia. > 250mm cannot
Φ300mm GraFlow
Φ100mm GraFlow

## Slide 54: Functional examples: Go through the Beam B
Formatted input

## Slide 55: Functional examples: Go through the Beam B
Program output
Visualization step (without Revit): we draw all the pipes in an array, for the figuring
这里放数字那个图

## Slide 56: Functional examples: Go through the Beam B
Program output
Flag3：水管直径小于250mm穿梁
GraFlow_1直径不足250mm，进行穿梁处理
GraFlow_2下折绕梁
Flag0：管线与梁冲突

## Slide 57: Functional examples: Go through the Beam B
Program output
East Section
West Section
Plan
Φ300mm GraFlow
Φ100mm GraFlow

## Slide 58: Functional examples: Automatic aligning
Revit input data
East Section
West Section
Plan
Φ300mm GraFlow
300mmx3000mm MVAC
Problem: different types of pipes occupy same space

## Slide 59: Functional examples: Automatic aligning
Formatted input

## Slide 60: Functional examples: Automatic aligning
Program output
Visualization step (without Revit): we draw all the pipes in an array, for the figuring

## Slide 61: Functional examples: Automatic aligning
Program output
Flag1：单层空间不足
Gravity Flow and MVAC in two sides of the corridor
the pipes turn right/left along with the wall
GraFlow_3和MVAC_3排在第二层

## Slide 62: Functional examples: Automatic aligning
Program output
East Section
West Section
Plan
Φ300mm GraFlow
300mmx3000mm MVAC

## Slide 63: Algorithm output: case example
Revit input data
East Section
West Section
Plan
Φ250mm GraFlow
1000mmx400mm MVAC
Now we go back to this case and see how to tackle these problems:
  different types of pipes occupy same space
  Some law might be violated (e.g. 30m’ law)
  Might not be enough space (height)
2000mmx400mm MVAC
Φ250mm GraFlow

## Slide 64: Algorithm output: case example
Formatted input

## Slide 65: Algorithm output: case example
Program output
Visualization step (without Revit): we draw all the pipes in an array, for the figuring
这里放数字那个图

## Slide 66: Algorithm output: case example
Program output
beam

## Slide 67: Algorithm output: case example
Program output
Shows the Gravity Flow only
It goes through the beams, and continuously going dowm
Flag3：水管直径小于250mm穿梁
GraFlow_1直径不足250mm，进行穿梁处理

## Slide 68: Algorithm output: case example
Program output
Shows the MVAC only
It is larger than 250mm, thus run under the beams
Installation space is given between pipe and beams

## Slide 69: Algorithm output: case example
Program output
Flag0：两管十字交叉相撞，小管下折避开大管
MVAC_1下折避让MVAC_5
Flag6：管线排布高度不够，穿过假天花
MVAC_1下折穿过假天花

## Slide 70: Algorithm output: case example
Program output
For this pipe, there is no beam between the beginning point and end point, therefore, to save room, make it as high as possible

## Slide 71: Algorithm output: case example
Program output
Flag8：水管长度超过30m
GraFlow_2在从起点开始，长度30m处下降200mm

## Slide 72: Algorithm output: case example
Program output
Flag6：管线排布高度不够，穿过假天花
GraFlow_2穿过假天花，需要增加（123-101）*10mm=220mm高度
Flag3：水管直径小于250mm穿梁
GraFlow_2直径不足250mm，进行穿梁处理
30m’s law make the pipe goes down for 200mm, making such problem happened in a more severe way

## Slide 73: Algorithm output: case example
Program output
East Section
West Section
Plan
Φ250mm GraFlow
1000mmx400mm MVAC
2000mmx400mm MVAC

## Slide 74: Algorithm output: case example
Program output